## Slide 1
Non-Refractive Modulators for Coding and Capturing Scene Appearance and Depth
Ashok Veeraraghavan
Amit Agrawal
Ramesh Raskar
Ankit Mohan
Jack Tumblin

## Slide 2
Main Lens
Object
1D Sensor
 -plane
x-plane
Ray - Filter
Consider the plane parameterization of 2D light field l(x,)
Now Imagine we could attenuate each ray independently before its capture at the sensor

## Slide 3: Ray Filter
Ray filter can attenuate each ray independently.
It is selective both in space and in direction.
The selectivity of a ray filter can be further enhanced with wavelength and control in time.
The ray-filter can be programmed to achieve any Ray Modulation Function (RMF).

## Slide 4: Ray-filter LF camera
Ray-filter
Macro Pixel
Pixel
Let us capture a 100 X 100 X 5 X 5 light field using a 500 X 500 pixel camera. Here is a trivial solution.
First divide the sensor pixels into 5X5 pixel groups (called macro-pixels as shown in the figure above).
Use the ray-filter to selectively allow rays to pass through such that a different angular direction is sampled at each sensor pixel. The ray-filter blocks the other rays.
Light efficiency can be further improved by doing Hadamard coding.

## Slide 5: Practical Issues with ray-filters
Ray-filter is a hypothetical device. We do not know of any material that can provide selective attenuation in both space and direction.
BUT CAN WE GET A SIMILAR FUNCTIONALITY
WITH JUST MASKS AS ATTENUATORS?

## Slide 6: Pinholes based Light-Field Camera

## Slide 7: Pinholes based Light Field Camera
Microlens array replaced by array of pinholes.
Images due to adjacent pinholes do not overlap.
Very Light Inefficient – Most light is blocked by Mask. Very little light reaches the sensor. Very Low SNR.

## Slide 8
Main Lens
Object
1D Sensor
 -plane
x-plane
Consider the plane parameterization of 2D light field l(x,)

## Slide 9
In Fourier domain, the sensor image corresponds to a slice of the light field
fθ
fx
fθ0
fx0
Band-limited Light Field
1 D Sensor Slice
Fourier Light Field Space

## Slide 10
In Fourier domain, the sensor image corresponds to a slice of the light field
fθ
fx
fθ0
fx0
Band-limited Light Field
1 D Sensor Slice
Fourier Light Field Space

## Slide 11
Even though sensor has high bandwidth, it cannot capture the extra dimension of the light field
fθ
fx
fθ0
fx0
Band-limited Light Field
1 D Sensor Slice
Extra sensor banwidth
Extra sensor bandwidth

## Slide 12
We need to distribute the energy in 2D light field to 1D sensor plane
fθ
fx
Band-limited Light Field
1 D Sensor Slice
???
???
???
???

## Slide 13
Solution: Modulation Theorem
Make spectral copies of 2D light field
fθ
fx
fθ0
fx0
Modulation Function

## Slide 14
fθ
Modulated Light Field
fx
fθ0
fx0
Sensor Slice
Modulation Function
Such that the sensor slice can capture the entire light field information
Inefficient, but at least some copies produced via modulation are sensed by the sensor slice

## Slide 15
How to recover light field from sensor slice?
Simple reshaping in Fourier Domain
fθ
fx
Recovered Light Field

## Slide 16
Key Idea: Modulate the light field using a set of slanted impulses
fθ
fx
fθ0
fx0
Modulation Function
By designing the correct set of impulses compared to a train of impulses in the Pinhole design this camera is very light energy efficient.

## Slide 17
Such modulation can be achieved by simply placing a mask inside the camera!!
Main Lens
Object
Mask
Sensor
α = (d/v) (π/2)
d
v

## Slide 18
Relationship between primal and Fourier domain
Main Lens
Object
Mask
Sensor
fθ
fx
fθ0
fx0
Mask Modulation Function
α
α = (d/v) (π/2)
d
v

## Slide 19
Optimal mask location is given by alpha, depends on fθR, fθ0 and fx0
Main Lens
Object
Mask
Sensor
fθ
fx
fθ0
fx0
Mask Modulation Function
α
α = (d/v) (π/2)
d
v
fθR

## Slide 20: PinHole Array in Frequency Domain
Band-limited light-field is shown in (a)
Fourier Transform of a train of impulses is a train of impulses as shown in Figure (b).
Each impulse produces a copy of the band-limited light-field as shown in (b)
The modulated light-field is shown in (b)
The sensor takes a slice of the modulated light-field as shown by the yellow box.
Energy inefficient since several copies of the light-field produced via modulation are not sensed by the sensor at all.

## Slide 21
Heterodyne Light Field Camera
Pin-hole array camera lets in very little light
It is also energy inefficient since several copies of the light-field produced via modulation are not sensed by the sensor at all.
A new solution: make limite number of replicas

## Slide 22
fθ
Modulated Light Field
fx
fθ0
fx0
Sensor Slice
Modulation Function
Make only a limited copies of the bandlimited light field !
Energy efficient since every one of the copies produced via modulation is sensed by the sensor slice

## Slide 23: Optimal Sampling of Light-Fields
Suppose the band-limit function is not necessarily rectangular but is arbitrarily shaped. Can we design a modulator that can optimally sample this light-field.

## Slide 24
fθ
fx
fx0
Modulation Function with mask optimized to the shape of the bandwidth of the light field.
fx0 + fx1
fx0+ 2fx1+ fx2
fθ0
fx1
fx2
Band-Limit shape is Arbitrary

## Slide 25
fθ
Modulated Light Field
fx
fθ0
fx0
Sensor Slice
Modulation Function
Mask is composed of impulses. But they are not harmonics.
No overlap within the red box sensed by the sensor.
Light Field copies overlap outside sensed region.

## Slide 26
fθ
fx
Recovered Light Field
Demodulation from Sensor Slice

## Slide 27
Fourier transform of optimal 1D mask pattern is a set of 1D impulses
Optimal 1D Mask is sum of cosines
Optimal 2D mask: Sum of cosines in 2D
Number of angular samples = Number of impulses in Fourier transform of the mask along that dimension

## Slide 28
A 2D camera that can capture 4D light fields!
2D Sensor image
Video showing refocusing from 4D light field
VIDEO HAS SLOW FRAME RATE FOR BETTER VISUALIZATION OF REFOCUSSING RESULT

## Slide 29
as well as high resolution image of focused parts of scene
High resolution image of in focus parts of the scene

## Slide 30
Using only a mask placed inside the camera
No additional optics
Main Lens
Object
Mask
Sensor

## Slide 31
Zoom in of the cosine mask
1/f0
Mask is the sum of cosines with four harmonics. Plot shows the cosines. Since the physical mask cannot have negative values, a constant needs to be added.

## Slide 32
Results
2D Sensor image
Zoom in showing the effect of cosine mask

## Slide 33
Computing 4D Light Field
2D Sensor image, 1629*2052
2D Fourier Transform, 1629*2052
FFT
Reshape 2D tiles into 4D planes
181*228*9*9
4D IFFT
4D Light Field
9*9=81 such tiles
181*228*9*9

## Slide 34
Refocusing: Take slices of 4D Fourier transform
2D Fourier Transform
2D FFT
Reshape 2D tiles into 4D planes
Take a 2D Slice
2D IFFT
181*228 refocused image
181*228*9*9
2D Sensor image, 1629*2052

## Slide 35: Views Demonstrating Parallax

## Slide 36: Extract Depth and All-in-focus
Recovered Refocussing
Depth Map
All in Focus
Variance Analysis

## Slide 37: Texture Mapped 3D surface
All In Focus Image
Depth Map
Texture Mapped 3D surface

## Slide 38: Tripod Refocussing
Captured Modulated Image
Refocussing Movie

## Slide 39: Extract Depth and All-in-focus
Recovered Refocussing
Depth Map
All in Focus
Variance Analysis

## Slide 40: Texture Mapped 3D surface
All In Focus Image
Depth Map
Texture Mapped 3D surface

## Slide 41: Mamiya Data Refocussing Video

## Slide 42
Focus on Scotch Magic

## Slide 43
Focus on Ambulance

## Slide 44
Focus on Doll

## Slide 45
Focus on Girl Right

## Slide 46
Focus on Girl Left

## Slide 47: All Focus Image