## Slide 1: Accelerometer-Based, Grip-Free Controller
Tyler (You-Chi) Le
ECE4220
Fall 2011
Dr. DeSouza
December 5th, 2011

## Slide 2: A Quick Overview
What is the project?
  A glove-integrated sensor that detects hand orientation using real-time tasks to provide control various applications
  Aimed to demonstrate a flexible and dynamic alternative to the traditional controller and joystick
  Prototype for demonstrations for both gaming and vehicular control for disabled persons
  Two simulation programs demonstrate potential usage

## Slide 3: Purpose
Provide a flexible, cheap, and dynamic controller for operation of vehicles, simulations, and games
Integrated with glove to replace fixed-shaped joysticks
Motion-based controls for ease of use
Configurable sensitivity to accommodate varying ranges of motion
Packaged with two graphical simulations to demonstrate potential usage and applicability

## Slide 4: Motivation (Background)
For disabled individuals:
  Current camera-based and optical motion sensors need min. distance and proper lighting, not appropriate for inside of cars or inside of confined spaces
  Present joysticks are limited by design shape and have limited usability
  Many joysticks require gripping an object rather than hand movement (May prove troublesome for people with lack of grip strength or finger damage/injuries)
  Desire to provide a easy-to-configure, easy-to-use prototype for vehicle control (possibly for wheelchairs or cars)

## Slide 5: Motivation Cont.
For video game control:
  Game system controllers are limited by design shape and have limited usability in representing different types of motion
  Minimum distance for optical sensors not applicable for PC’s as users have to be close to keyboard and mouse
  Joysticks and driving wheels are costly and single-purposed

## Slide 6: Proposed Implementation
Hardware:
  Detect hand orientation using an analog 2-axis accelerometer
  Accelerometer is affixed to top of glove, no finger grip necessary
  Power drawn from TS-7250 DIO lines
  TS-7250 on-board ADC measures analog output of accelerometer to measure tilt/orientation*
  *MAX197 Add-on is not available on TS-7250’s in lab

## Slide 7: Integrated ADC on TS-7250
Integrated ADC
5 Channels
MAX197, not avail. In current lab TS-7250

## Slide 8: Hardware Block Diagram
2-Axis Accelerometer
ADC and TS-7250 Embedded System
Network Server
Linux Terminal

## Slide 9: Proposed Implementation
Software:
  Control registers for ADC as well as ADC results are mapped to the compiler using mmap() and provided addresses
  Four pthreads initialize real-time tasks that operate in sequence to produce graphical simulations based on hand orientation
  Real-time tasks operate with 0.1 second periods for 10 Hz axis measurements, simulation update, and graphic output
  Character array-based graphics printed through the Linux Terminal for graphical output
  User-configured range of motion at initialization for varying sensitivity

## Slide 10: Proposed Implementation
Real-time (RT) Structure:
  Two RT tasks poll the output of the 2-axis accelerometer and store result into two shared buffers
  A third RT task reads from the shared buffers to update graphical positions of various simulation components
  Fourth RT task prints the updated character arrays to the Terminal, producing the graphical display
  Each task prevents the next successive task from execution before completion using semaphores

## Slide 11: Software Block Diagram
Shared Buffer
Measure H-Axis
Measure V-Axis
Shared Buffer
SEM1
SEM2
Update Graphics
SEM3
Display Graphics

## Slide 12: Real-Time Concepts Used
Pthreads – multithread operation
Periodic RT tasks
Semaphores
Shared buffer
Producer-Consumer Structure
I/O Polling
Priority Scheduling

## Slide 13: Results
  TS-7250 produces measurements and displays consistent with hand motion
  Simulations demonstrate both practical usage and gaming application for proposed prototype
  User-defined minimum and maximum values allow customizable range of motion
  The prototype cost around $15 dollars excluding the TS-7250

## Slide 14: Potential Improvements
  Migrate functionality to the MAX197 Optional Add-on ADC for better accuracy and faster sampling
  Better accuracy would result in better resolution, allowing smaller minimal range of motion
  Expansion of buffer and threads to allow 6 axis, both-hands operation
  Utilizing display drivers or programs that minimize processing speed to allow faster refresh rate
  Implementation to prevent unintentional acceleration through averaging algorithms
  Wirelessly integrate ADC and accelerometer

## Slide 15: Potential Implementations
  Placed on hand, head, and/or fingers to sense orientation for vehicular control for disabled persons
  “Makeshift” joystick similar to Nintendo Wii controllers, but with no required physical hardware to grip
  Robotics control
  Transport what is already available on many mobile devices to larger-scale applications

## Slide 16: Conclusion
  Demonstrates a flexible and configurable prototype for a non-conventional controller
  Provides a motion sensing module that does not require grip and holding an object
  Potentially beneficial towards people with disabilities lacking a large range of motion or grip strength
  Demonstrates potential to replace a wide variety of single-purpose video game joysticks (cost-saving)
  Can be used in confined spaces on systems larger than mobile devices
  Successfully demonstrates usage of real-time design in simulation and controller

## Slide 17: Questions?