## Slide 1: Real-Time CAN bus Data-logger
Matthew Nevels
ECE4220
5/3/2010

## Slide 2: What I did
Display & Record live performance data
Formula SAE team uses CAN protocol for inter-module communication on the car.
NI CompactRIO donated to the team
  Intel Processor, CF disk, ethernet
  Xilinx FPGA
  CAN communication module
  IntervalZero’s PharLap ETS real-time OS

## Slide 3: How I did it
FPGA
CAN Module
Send CAN Packets
Receive CAN Packet
Phar Lap RTOS
SetTimings & Data Requests
Parse CAN Packet Data
DMAFIFO
Windows Client
FTP Download Data File
Start/Stop Logging
Record to
Data File
Display Live Data
WWW/FTP Server
Graph/Analyse Data
Control/View Logger
Microcontroller
Microcontroller
Microcontroller

## Slide 4: Results
CompactRIO only has input modules…
  Used an Atmel module:
    When CAN interrupt is triggered, pulse an output
Added code to the Datalogger:
  Thread that repeatedly creates an array of 1 million doubles & then computes their FFT.
  Added a control to enable/disable this added load

## Slide 5: Results
Used an Oscilloscope to measure actual CAN packet reception timing.
  Ran Datalogger at various frequencies from 1Hz to 500Hz.
  While Oscillscope was showing the measured frequency I enabled the additional load and saw no change in packet timing.

## Slide 6: Conclusions
Formula SAE Team now can view and record Live data.
  Better optimize the tuning of various components.
LabVIEW makes Real-Time Real-Easy.