## Slide 1: Infrared Security System
Clark Buckles
Real Time Embedded Systems

## Slide 2: Topics
Problem Statement
Parts Used
Class Topics Implemented
Implementation
Conclusion
Questions

## Slide 3: Problem Statement
Security is a very important part of businesses as well as Universities
The goal is to implement a simple security system using the tools we learned in class
Be able to control and monitor multiple room sensors from a single location

## Slide 4: Parts Used
TS-7250
  Digital input/output port
  Outputs 3.3V
  Logic 0 = 0V Logic 1 = 3.3V
Auxiliary board provided in class
  5 push buttons, 3 LEDs, and speaker
Passive Infrared Sensor
  3 to 6 V Vcc
  Short and long range settings
  Outputs 0 or 3.3V
  Output based on motion
  40 second warm up

## Slide 5: Class Topics Implemented
Real Time Function
  Sample PIR input every 1 second
Hardware interrupt
  Change the message sent to the server program
FIFO Data Structures
  Communicate between kernel modules and user space
    Real time function to server
    Output status of PIR
Socket
  Udp communication between the server and all clients
    Server broadcasts message
    Data packets of 20 characters

## Slide 6: Implementation
Block Diagram
Server Program and User Display
Client Program
Kernel
Kernel Rt_task
Client Program
Kerenel
PIR Sensor
PIR Sensor
Socket
Auxiliary Board
FIFO
FIFO
FIFO

## Slide 7: Implementation
Kernel Real Time Task
  Sends message to client program every 1 second through FIFO
  Uses a hardware interrupt to change message sent to server
    Status, Activate, Deactivate
Server program
  Broadcasts message to all servers programs
  Receives Data from all connected servers
  Updates room status’ and displays to user

## Slide 8: Implementation
Client Program
  Receives broadcasted message from the server
  Classifies message
    What room is being signaled
    What should it do
  Determines message to be sent back to server
    Gets status of PIR from kernel module
Kernel Module
  Checks status of input
  Sends to server by FIFO

## Slide 9: Implementation
If sensor 1 is turned off:
Status OFF
Sensor 1 is activated:
Activate1 UPDATING
Status WARMING UP (40 seconds)
Status NORMAL or DETECTION

## Slide 10: Conclusion
Problems retrieving input from PIR sensor
Future Work
  When not in security mode use sensor to control the lights of the room
  Include camera system for when movement is detected

## Slide 11
Questions