## Slide 1: Automatic License Plate Recognition(ALPR) on embedded system
Presented by Guanghan

## Slide 2: applications
Automatic toll collection
Traffic law enforcement
Parking lot access control
Road traffic monitoring

## Slide 3: ALPR system: several stages

## Slide 4: My research in the real-time embedded system project
Hardware part:

## Slide 5: My research in the real-time embedded system project
The "main board" performs segmentation on license plate images. Its auxiliary board provides time to capture/load license plate images.
"Child boards" need to receive segmented characters from the "main board". The characters are transmitted through ports.
The "child boards" will recognize the character received and then send the recognized number back to the "main board" through ports.
The "main board" exhibits the recognized numbers.

## Slide 6: My research in the real-time embedded system project
Software part: main board

## Slide 7: My research in the real-time embedded system project
The "main board" side
The module for the "main board" will check the B0 button of its auxiliary board.
Once B0 button on the auxiliary board of the TS-7250 "main board" is pressed, which simulates the process of this Vehicle retrieval system capturing the image of vehicles, the module will send the message through a fifo to the main thread, who will then read license plates from a pre-defined directory. The main thread will thereafter perform segmentation of the plate.
The user space program for the "main board" have three set of threads. Aside from the main thread mentioned above, one set of threads will ask from the main thread for the segmented characters through a shared buffer, then send the segmented characters to "child" boards via the ports.
Another set of threads will do the job of receiving recognized numbers from "child boards". Once the numbers are received, the threads send them to the main thread through several named pipes.
Once the main thread receives the recognized numbers, since it knows which number comes from which thread, it then prints out the numbers in the same order as they are shown on the plate. Semaphores will be used as a form of synchronization. The main thread only prints out the results after the threads that send the numbers are synchronized.

## Slide 8: My research in a real-time embedded system project
Software part: child board

## Slide 9: My research in a real-time embedded system project
The "child boards" side
There are two threads for the user space program(for each of the child board). For each child board, one thread receives the corresponding character from the "main board", put them in a shared buffer. The other thread reads from the shared buffer the segmented character, perform character recognition, and then send the recognized number back to its corresponding "main board"-thread.

## Slide 10: My research
1. License Plate extraction
Scan the whole image.
Canny edge detection to find possible regions.
Extract HOG features from these possible regions.
SVM to classify whether one block contains license plate.
K-means to merge nearby possible regions.

## Slide 11: My research
1. License Plate extraction

## Slide 12: My research
1. Licence Plate Extraction
Use edge information. Only scan regions with edges. (Cut time half.)
Use correlation between scales. Information transfer to the next scale through a size-deformable cascade mask.( Cut another half)

## Slide 13: My research
License Plate Extraction
Regions that are covered by the scan. Rectangle is plate-size. Will Merge.

## Slide 14: MY research
License Plate Extraction
Scan region: Large amount of time is saved. 250ms for two scales.

## Slide 15: My research
2. Alignment
Align the four lines of the plate so that the ROI fits the plate contour very well.
Use Color information.
Align

## Slide 16: My research 2. Alignment

## Slide 17: My research 2. Alignment
score= dist_RARC- weight_left*dist_RCRB
score= dist_RARC- weight_right*dist_RCRB
score= dist_RARC- weight_up*dist_RCRB
score= dist_RARC- weight_down*dist_RCRB + dist_RARB;
RGB hitogram
distance

## Slide 18: My research
3. Segmentation
Use prior knowledge: Know how many characters exist in a license plate.
A corresponding model.
Use k-means to binarize the aligned plate.
Optimize the score.
Scan vertically. In model’s character region if black score adds, in space region if black score decreases.

## Slide 19: My research

## Slide 20: My research 2. segmentation
Threshold to binary
No threshold
Scan vertically.
0 to 255 change: ct++

## Slide 21: My research 2. segmentation
Prior Knowledge
Segmentation model

## Slide 22: My research
4. Recognition
Features:
0 to 1 changes in each column
0 to 1 changes in each row
1 ratio in each column
1 ratio in each row
Raw feature
Classifier:
SVM

## Slide 23: My research Results:
Based on 62 test images.
Detection rate: 100%
Segmentation: 100%
Recognition: 99%