## Slide 1: Logic Analyzer
ECE-4220 Real-Time Embedded Systems
Final Project
Dallas Fletchall

## Slide 2: Objectives
Determine Logic Level of multiple signals
Graphical Display of Results
  Tabular formatted data is hard to quickly interpret
  Signal labeling improves the ease in determining system performance
Adjustable voltage levels
  Allow for multiple systems with different thresholds to be analyzed

## Slide 3: Implementation
Client-Server Model Responsibilities
Client
  Requests data collection to begin
  Requests changes in voltage thresholds
  Display data graphically using GnuPlot Software
  Responsible for user interface
Server
  Respond to requests from Client
  Collect data on the GPIO pins and send across network
  Reformat voltage change requests for DACs
Signal Conditioning
  Provide high impedance while sampling input signals
  Provide variable voltages to comparator circuits

## Slide 4: Implementation
Signal Conditioning
Provide high impedance to input signal
  Reduces the loading effect from measuring the signal
Limit the voltage output
  Ensure voltage input to data collection server is within tolerance
Allow for comparison for voltages outside tolerance of data collection Server

## Slide 5: Implementation
Server Hardware
Raspberry Pi chosen as data collection server
  Has 700Mhz processing core
  Less than $40 cost
  Available Linux Distributions to handle system calls, and decrease development time
  Well documented on the web
  16 general purpose input/output (GPIO) pins
Orsini, Lauren. The front of a Raspberry Pi Model B. [Photo].
Retrieved from : http://readwrite.com/2014/01/20/raspberry-pi-everything-you-need-to-know

## Slide 6: Implementation
Client Hardware
Need display capabilities
Network connection
GnuPlot Software

## Slide 7: Implementation
Server Software
Message Handling
  Start sampling message
  Configure DAC settings
Data collection
  Setup and read GPIO pins
  Determine starting and stopping times
  Send register value to Client for each sample
  Send elapsed time to Client after sampling completion
DAC Communication
  Handle SPI communications

## Slide 8: Implementation
Client Software
GnuPlot Display
  Handle channel labeling
  Update plot after recording
  Set x & y axis labels
User Input
  Display options menu
  Format user input
    Server expects messages in certain format
    Abstract how GnuPlot system works from user
  Relay error messages

## Slide 9: Results
Sampling Rate
  333k samples/sec average
DAC accuracy
  +-19.5mVdc
Graphical Display of Collected Data
Reliable Network Connection

## Slide 10: Results

## Slide 11: Experiments/Discussion
Sample Rate
Initial Implementation
Server stored struct timeval and an int for each channel
File was transmitted using system call, sendfile()
Advantages
Removed unnecessary implementation details from client application
sendfile(), according to man pages is supposed to be the most efficient way to transfer files
Disadvantages
Storing to a file on rasperry pi is extremely slow.
  Writing to the file without sending restricted sampling rate to approximately 200k samples/sec
Each GPIO was masked and shifted individually

## Slide 12: Experiments/Discussion
Time Taken to Record 300k Samples to File on Server
Time Taken to Send 300k Samples over Socket
VS.

## Slide 13: Experiments/Discussion
WiringPi
Open source library
Easy access to GPIO pins and special functions
Problems
To support all versions of raspberry pi, conditional statements for board revision and pin numbering scheme are used
GPIO read entails bit masking and shifting, returning a single pin value.
8 reads necessary to determine channel values compounded unnecessary instructions
WiringPi renamed the GPIO pins to ease use, but consecutive pins were not necessarily consecutive in the GPIO level register

## Slide 14: Experiments/Discussion
WiringPi Pinout Scheme
Henderson, Gordon. WiringPi pinout scheme. [Table].
Retrieved from : http://wiringpi.com/pins/

## Slide 15: Experiments/Discussion
Sample Rate
Improvement
Remove calls to wiringPi API
Read and store the entire GPIO level register
Advantages
Register could be read and stored, handling masking and shifting after sampling
Removes all conditional statements
Removes need to read register value, masking, and shifting for each pin individually
Disadvantages
Difficulty setting the pin function, such as input/output, special function selection, pull-up/pull-down resistor

## Slide 16: Experiments/Discussion
Implications of GPIO Selection
Advantages
Selecting 2 separate consecutive four pins allowed for less computation to mask and shift
Required less pins without need for SPI connections
Disadvantages
Serial Peripheral Interface pins were unavailable for use
  Software mimicked this interface to allow for communications with DAC

## Slide 17: Experiments
Sample Rate Experiments
Transmit Package Size
Create a buffer of multiple GPIO level register values and send buffer over the socket
Advantage
Maximum number of samples able to be recorded, approximately 400k samples/sec
Disadvantage
Increased samples were in bursts, with gaps in recorded data

## Slide 18: Experiments
Example of gaps in collection
using multiple register readings
sent over the network.
The text above is the file being
plotted.

## Slide 19: Experiments
Sample Rate Experiments
Estimate Time of Sample
Determine sample time by equally spacing samples across total time to record all samples
Advantages
Package size decreased
Times can be calculated after sample collection
Disadvantages
Sample time accuracy not guaranteed

## Slide 20: Conclusion
Failures
Sampling rate is too slow for use with serial data transfer
Real-Time system would improve due to accurate spacing between recordings.
Long interval sampling reduces accuracy
Successes
Data was able to be plotted graphically
Correct collection and display of data
Increased sampling rate can be achieved for small time intervals